## Slide 1: CTA: CERN (CASTOR) Tape Archive Rationale and Status
Germán Cancio, Daniele Kruse, Eric Cano, Steven Murray

## Slide 2: A talk in two parts
What is CTA - Presented by Eric Cano
Requirements of a tape storage system
Architecture of CTA (CERN/CASTOR Tape Archive)
Rationale and status - Presented by Steven Murray
Rationale
The prototype / proof of concept
What’s next

## Slide 3: Main characteristics of tape
It’s cheap, safe, power efficient
Media is the biggest cost driver
Tapes can be reformatted to higher density when newer drives come out
High throughput
  360MB/s per drive today, 1GB/s already in the roadmaps
High capacity
  7-10TB per tape, 220TB demonstrated in labs
  About 8 hours to fill or read a complete tape
High latency
  Tape mount and unmount take ~30s/1min+ each
  Full tape seek ~30s
  This does not improve with new equipment
Sequential access
Low concurrency
  Limited number of tape drives in the library
Locality and format constraints
  Drive only mount tapes from their own library and right format

## Slide 4: Our infrastructure and forecast
2 vendors
7 libraries (~70k slots)
~30k tape (7-10TB each)
80 drives (250-360MB/s)
Expected load for the coming years
  2016 last cool year (40PB to write, as much to verify, plus user reads)
  From 2017 on write 120-140PB/year (multiply by 2-3 for reads)
  Repack and verification are high volume, low priority tasks
    Should yield drives to user activity

## Slide 5: Requirements for tape efficiency
Mounts should be made worthwhile
  1 mount operation  20GB of bandwidth
  Queue file transfers until we have enough data to transfer
Single step mount decision for tape-drive couple
Drives should run full speed
  Buffering in memory (12-64GB/drive) absorbs glitches
  Disk system should achieve proper average
Drives should run all the time
  Repack and verification should fill all idle drive time
  … but also yield to experiment activity
Data has to be repacked regularly
  Allowing re formatting of media
Data needs to be verified
  Detection of problem tapes

## Slide 6: Jobs queues
tapeserverd
tapeserverd
Tapepools
Tapes
Tapeserverd
Retrieve jobs queued via front ends
Tape servers pulls retrieve jobs from
the queue in shared storage
Archive jobs queued via front ends
Tape servers pulls archive jobs from
the queue in shared storage
tapeserverd
tapeserverd
Tapeserverd
Queue sizes (file sizes and count) are used for mount decision
Tape pool is chosen through archive routes
Tape is bound late to drive: no tape stuck with no compatible drive available

## Slide 7: Global architecture
Remote
storage
CTA
tape server
CTA
tape server
CTA
front-end
CTA
command-line
tools
CTA
command-line
tools
CTA meta data store
Tape catalogue
Drive status
Hardware layout
Queues
Tape pools
Mount policies
Drive capabilities
Routing
CTA
Client commands
CTA
front-end
CTA
tape server
Archive
namespace
EOS
Evolved from CASTOR
All of the CTA business logic and data management code is in the client interface to metadata
Two prototypes
Ceph
Local file system
Data
Commands/control
Disk
Disk
Tape
Tape
Tape
Disk
Disk
Tape
Tape
Tape

## Slide 8: Rationale for CTA
Less daemons
  CASTOR
    5 types of daemon
    stagerd + tapegatewayd + vmgrd + vdqmd + tapeserverd
  CTA
    2 types of daemon
    xrootd (front end) + tapeserverd
Tapes and drives can be scheduled simultaneously

## Slide 9
tapegatewayd
vdqmd
vmgrd
stagerd
1. Schedules a archival mount based because:
  There are enough files OR
  There is enough data OR
  A pending file is too old
2. Requests a free tape from the destination tape pool
3. Locks the tape for write access
4. Queues a request for drive compatible with the chosen tape
tapeserverd
5. Sends the job to the drive
Scheduling a CASTOR archival
Tape
Organic/legacy system resulting in 5 types of daemon
Partial decisions made by different daemons results in tape being chosen independently of drive
Generates needless queues on busy drives whilst other eligible drives are idle
Organic/legacy system resulting in 5 types of daemon
Partial decisions made by different daemons results in tape being chosen independently of drive
Generates needless queues on busy drives whilst other eligible drives are idle

## Slide 10: Scheduling a CTA archival
Scheduler object store
tapeserverd
Tape
Pull the next eligible tape to be mounted
Single step “pull” scheduling using only a single type of daemon
Tape and drive scheduled simultaneously
Workload is naturally load balanced across eligible drives

## Slide 11: Rationale for CTA
Simpler solution for a simpler problem
No need to support random access
  Tape access has evolved from random access to bulk archival and retrieval
Centralized disk scheduling no longer needed
  Distributed striped file systems now exist
  Only really need to prioritize tape streams
  Can concentrate on scheduling tape

## Slide 12: Rationale for CTA
Less wire protocols
  Will follow the EOS approach of using XrootD
All scheduling information in one place
(hardware catalogues, queues, policies)
  Global view
  Easier to understand
  Easier to improve
  Easier to maintain
Support preemptive scheduling
  Throttle repack and tape verification
  Use drives 100% of the time with little operator effort

## Slide 13: Rationale for CTA
Avoid duplication of disk management between CASTOR and EOS
Preserve the knowledge and code driving the tape hardware from CASTOR
System boundary between EOS and CTA
  Clean separation of concerns
  Independent EOS and CTA releases
Simpler system to operate
  Less daemons
  Tape operators responsible for stager disks

## Slide 14: CTA prototype
What was in the prototype
End user and admin command-line tools
Frontend server – A CTA plugin for xrootd
Ported tapeserverd from CASTOR to CTA
Central object store for scheduling
  Hardware catalogues
  Policies
  Queues

## Slide 15: CTA prototype
What was shown by a demo of the prototype
Archived files from EOS to tape
2 tape drives were used in parallel
Each EOS file had two tape replicas
Retrieved the file back from tape to EOS
Provided a user interface targeted at end users and at administrators

## Slide 16: CTA prototype
CTA commands used during the demo
  cta logicallibrary add -n IBM1JB -m "the test lib"
  cta tapepool add -n cms -p 15 -m "CMS raw"
  cta tape add -v I21748 -l IBM1JB -t cms -c 1000000000000 -m "A cta tape"
  cta tape add -v I21805 -l IBM1JB -t cms -c 1000000000000 -m "A cta tape"
  cta tape add -v I21902 -l IBM1JB -t cms -c 1000000000000 -m "A cta tape"
  cta storageclass add -n single -i 2 -c 1 -m "A single copy class"
  cta archiveroute add -s single -c 1 -t cms -m "Route to cms"
  cta mkdir /cms
  cta setstorageclass /cms single
  cta archive "eos://eos/cms/smallfile" /cms/smallfile
  cta ls /cms
  cta listpendingarchives
  sleep 60
  cta ls /cms
  cta retrieve /cms/smallfile "eos://eos/cms/smallfile_retrieve"
  cta listpendingretrieves
Admin commands
File commands

## Slide 17: What’s next
Conclusions from architecture meetings
  Several models and approaches were discussed within the section and group
  Models ranged from
    Putting CTA on the back of EOS
  Through to
    A new orchestrator in front of EOS and CTA
Similar systems were studied and in particular the IBM Spectrum Archive Solution (GPFS)
Will now concentrate on putting CTA on the back of EOS

## Slide 18: What’s next
EOS
Workflow engine
EOS
Workflow engine
EOS at the front – CTA hidden from end users
CTA frontend
One EOS instance for each LHC experiment plus one for public users
Each EOS instance is responsible for the namespace of its users
Archive file and tape catalogue
Scheduler object store
Critical information about tape files and tapes
Scheduler queues and policies
Tape
tapeserverd
Tape
tapeserverd
Tape
tapeserverd
EOS
Workflow engine

## Slide 19: What’s next
Modules to be developed
Archive file and tape catalogue
Production version of scheduler object store
Functionalities to be developed
EOS workflow engine to CTA glue
Repack
Tape verification
EOS to CTA reconciliation engine
Operations scripts and procedures

## Slide 20: What’s next
Migration strategy from CASTOR to CTA
CTA uses the same tape format at CASTOR
No need to transfer data
Only need to transfer metadata
Many possibilities still under discussion
  Transfer one experiment at a time
  Transfer one tape pool at a time
  Transfer one tape at a time
  Transfer based on the namespace